## Slide 1
Optimal Design for Improving Drag and Cooling Performance of
KSAE E-Mobility through CFD Analysis
G. H. An, C. S. LEE
Handong Global University Mechanical Control Engineering
Introduction
Purpose: Improve driving performance and cooling of electronic devices of KSAE E-mobility
Objective: To minimize the flow separation phenomenon (Fig 1), the vehicle was designed with a streamlined shape to reduce the drag coefficient and decrease the vehicle frontal area
Model Description
Advanced 1 (Frame Unmodified)
Advanced 2 (Frame Modified)
Fig 3. NACA 4412 (XFOIL)
Fig 4. NACA 2412 (XFOIL)
Fig 5. NACA 4412 (XFOIL)
The model was inspired by the Power 0.5 model of Nose Cone Design (1), and the front part of the vehicle was designed with a streamlined shape.
Fig 5. Original, Advanced 1, Advanced 2 Models (Up view)
Model Comparison
Fig 6. Advanced 2 Model Sketch (NACA 2412)
RRH
NACA 2412
Driver
Turbulence Model & Boundary Conditions
CFD Result (Drag Force)
CFD Result (Cooling)
Wind Tunnel Experiment
z
Discussion & Conclusion
Type | Condition | Speed
Inlet | Velocity-Inlet | 20 [m/s]
Outlet | Pressure-Outlet | -
Cowl | Stationary-Wall | -
Frame | Stationary-Wall | -
Wheel | Rotational | 87.489 [rad/s]
Ground | Translational | -20 [m/s]
Tunnel-Wall | No Shear | -
Used Turbulence Model: Spalart-Allmaras (1-eqn)
Single Transport Equation -(3)
Suitable for External Boundary Layer Flow Analysis
Low Computational Cost
Table 4. Boundary Conditions used in CFD Simulation
The design is based on the NACA 2412 airfoil (at AOA, ), which has a low lift-to-drag ratio, and the smallest drag coefficient .
The driver's seating position was changed from a sitting posture to a 30 reclining posture, reducing the height of the RRH by 350mm.
Meshing Method
Region | Type | Size (mm)
BOI-nearfield | Body of Influence | 40
BOI-farfield | Body of Influence | 90
Bumper and Rods | Curvature | Min:4 / Max:5
Cowl | Curvature | Min:5 / Max:30
Wheel | Curvature | Min:3.5 / Max: 5
Boundary Layer | Last-ratio | 10 layers / Ratio: 0.2
Surface | Curvature & Proximity | Min: 0.5 / Max: 256
Volume | Poly-hexcore | Min: 0.5 / Max: 512
Table 3. Mesh Conditions
Fig 2. Power 0.5 Nose Cone Design
2513mm
2426mm
2194mm
Fig 1. Separation Phenomenon
Table 1. Lift-to-Drag Ratio and Drag Coefficient of NACA Airfoil at Different Angles of Attack
Fig 8. Surface Mesh (Left), Volume Mesh (Right)
Fig 7. Mesh Convergence
Power [KW] | 8.6
Torque [Nm] | 33.9
[rad/s] | 254.59
Wheel Radius [m] | 0.115
 | 17:50
[kg] | 250
 | 0.7
 | 0.85
Power [KW] | 8.6
Torque [Nm] | 33.9
 | 254.59
Wheel Radius [m] | 0.115
 | 17:50
 | 250
 | 0.7
 | 0.85
Table 5. DIY Car Spec Sheet
 | Original Model | Advanced Model 1 | Advanced Model 2
 | 0.40 | 0.385 | 0.3
 | Original Model | Advanced Model 1 | Advanced Model 2
 | 0.40 | 0.385 | 0.3
Fig 9. Velocity pathlines and Pressure Contour of Models
Fig 11. Rear Cowl Velocity Contour (Original, Advanced 1, Advanced 2)
Fig 10. Drag Force and Drag Coefficient
By adding an air vent shape, fast-flowing fluid through a narrow passage cools the electronic device with lower temperature fluid. (
Electronic device
Electronic device
Electronic device
Drag force reduced by 21.1% for Advanced 1 model and by 43% for Advanced 2 model.
Drag Coefficient reduced by 17.7% and 21%.
RRH(Rear Roll Hoop) and front wheels caused the most drag, due to vortices in rear area.
Streamlined design for advanced models reduced the drag coefficient.
Reduced frontal area mostly contributed to reduction of drag force.
Air vent drag did not significantly impact overall drag.
Air Vent
Fig 12. Wind Tunnel Experiment
The reduced drag (105[N]) is significant compared to the traction force of the vehicle (515.87[N]) in Table 5.
Reducing the projected area and drag coefficient resulted in decreased drag force.
Reduced drag can improve top speed and acceleration.
Safety device (RRH) regulations limited drag force reduction up to 43%.
Adding air vents improved cooling and motor efficiency.
Simulation time: 90min. Proper geometry and mesh generation are crucial (16-core process, 2.9 million cells).
Table 2. Projected Area of Models
Fig 16. Drag Force & Drag Coefficient (8.6[m/s])
Fig 13. Comparison of Experimental and Simulation Results
Original Model
Advanced Model 1
Advanced Model 2
Original Model
Advanced Model 1
Advanced Model 2
Original Model
Advanced Model 1
Advanced Model 2
Original Model
Advanced Model 1
Advanced Model 2